State of Arkansas

OFFICE OF STATE PROCUREMENT

1509 West Seventh Street, 3RD Floor

Little Rock, Arkansas  72201-4222

501-324-9316

ORDERING INFORMATION FOR SP-09-0148; HYBRID VEHICLES

==================================================================================

BUYER: Julia Shackelford @ 501-371-6079 or Lee Costley @ 501-324-9318

==================================================================================

CONTRACT PERIOD: JANUARY 1, 2009 THROUGH DECEMBER 31, 2009 or factory cut-off dates for each item, whichever comes first.  Cut-off dates are established by the manufacturer and begin as early as January or as late as August. Upon mutual agreement, contract for individual items may be extended up to two (2) additional years, or a portion thereof in accordance with the terms of the original contract.

==================================================================================

CONTRACT AWARDED TO:

ITEM 2:

Cardinal Chrysler Jeep Dodge Toyota

Attn: David Sedgwick, Fleet Manager

2740 Whitten, Suite 120

Memphis, TN  38133

Phone: 901-488-0980

Fax: 901-381-1491

E-Mail: dsedgwickfleet@bellsouth.net

ITEMS 5 & 6

Bale Chevrolet

Attn: David Broyles, Fleet Manager

13101 Chenal Parkway

Little Rock, AR  72211

Phone: 501-221-9191

Fax: 501-221-7418

E-Mail: dbroyles@balechevrolet.com

ITEMS 8 & 10

Longo Toyota

Attn: Roy Durham Jr, Corporate Fleet Director

3534 N. Peck Road

El Monte, CA  91731

Phone: 626-580-6048

Fax: 626-580-6137

E-Mail: roy.durham@longotoyota.com

ITEM 2: TYPE HMH - MID-SIZE HATCHBACK SEDAN, 4-CYLINDER

AASIS MATERIAL # 10123537

VENDOR: CARDINAL CHRYSLER JEEP DODGE/100047104

MFG & MODEL BID: Toyota Prius (1224)					$22,757.15

ENGINE & CYLINDERS: 1.5L/4-cylinder

PRODUCTION MONTH: April 2009

Approximate Delivery after production date: 240 days

Air Bags: Driver & Front Passenger, factory installed

Air Conditioning: factory installed

Alternator: type recommended by manufacturer for vehicle as equipped.

Battery: Ni-MH (Nickel-Metal Hybrid)

Battery Voltage: type recommended by manufacturer for vehicle as equipped

Brakes: Each vehicle shall be equipped with the manufacturer's standard power assisted service brakes with a four-wheel, electronic controlled, anti-lock brake system (ABS).

Doors: Four (4) manufacturer's standard type for vehicle

Emissions System: manufacturer's standard type for vehicle.

Engine: minimum of 4-cylinders

Floor Mats: front and rear, color to coincide with interior.

Glass: manufacturer standard privacy or tinted glass in all windows.

Horsepower, Net: minimum of 110 hp

Inside hood latch control

Keys: 2 sets

License Plate Brackets: front and rear

Operator's Manual

Paint: one (1) exterior color selected from manufacturer's standard list and specified by ordering entity.

Power Steering: factory installed manufacturer's standard power assisted steering

Radio: AM/FM

Seat, Front & Rear: type recommended by manufacturer for vehicle as equipped

Suspension: type recommended by manufacturer for vehicle as equipped.

Tires and wheels: (four) 4 radial, tubeless tires of the size and load range recommended by vehicle manufacturer for automobile as equipped.

Transmission/Driveline: Each vehicle shall be equipped with the manufacturer's standard automatic-overdrive type transmission and shall include the manufacturer's standard transmission cooler. Vehicles equipped with a continuously variable transmission (CVT) will be acceptable.

Upholstery: cloth material and colors to coincide with exterior color chosen.

Warranty, Basic: 3 years/36,000 miles

Warranty, Battery: 8 years/100,000 miles

OPTIONAL EQUIPMENT - Purchaser may choose from the following:

Body Side Molding	$125.00 dealer installed

ITEM 5: TYPE HTT - 1/2T CREW/QUAD CAB TRUCK, 2WD

AASIS MATERIAL # 10123534

VENDOR: BALE CHEVROLET/100095671

MFG & MODEL BID: Chevrolet Silverado Crew (CC10543) with Standard Hitch		$35,193.00

ENGINE & CYLINDERS: 6.0L/V8

PRODUCTION MONTH: January 2009

Approximate Delivery after production date: 8 weeks

Air Bags: Driver & Front Passenger, factory installed

Air Conditioning: factory installed

Alternator: type recommended by manufacturer for vehicle as equipped

Battery: Ni-MH (Nickel-Metal Hybrid)

Battery Voltage: type recommended by manufacturer for vehicle as equipped

Brakes: Each vehicle shall be equipped with the manufacturer's standard power assisted service brakes with a four-wheel, electronic controlled, anti-lock brake system (ABS)

Doors: Two (2) manufacturer's standard type for vehicle

Emissions System: manufacturer's standard type for vehicle

Engine: minimum of 8-cylinder

Floor Mats: front and rear, color to coincide with interior

Glass: manufacturer standard privacy or tinted glass in all windows

GVWR: 7100 lbs

Horsepower, Net: minimum of 295

Inside hood latch control

Keys: 2 sets

License plate brackets: front and rear

Operator's Manual

Paint: one (1) exterior color selected from manufacturer's standard list and specified by ordering entity

Payload package for heavy-duty use

Power Steering: factory installed manufacturer's standard power assisted steering

Radio: AM/FM

Seat, Front: 40-20-40 split bench

Seat, Rear Bench: full width, folding, 3-passenger

Suspension: type recommended by manufacturer for vehicle as equipped

Tires and wheels: (four) 4 radial, tubeless tires of the size and load range recommended by vehicle manufacturer for automobile as equipped

Towing Capacity: 6000 lbs

Transmission/Driveline: Each vehicle shall be equipped with the manufacturer's standard automatic-overdrive type transmission and shall include the manufacturer's standard transmission cooler. Vehicles equipped with a continuously variable transmission (CVT) will be acceptable

Upholstery: cloth material and colors to coincide with exterior color chosen

Wheelbase: minimum of 140"

Warranty, Basic: 3 years/36,000 miles

Warranty, Battery: 8 years/100,000 miles

OPTIONAL EQUIPMENT - Purchaser may choose from the following:

HD Trailer Towing Equipment for towing up to 6700 lbs		NA

HD Trailer Towing Equipment for towing up to 7700 lbs		NA

Limited Slip or Locking Differential		STANDARD

Body Side Molding				STANDARD

ITEM 6: TYPE HFT - 1/2T CREW/QUAD CAB TRUCK, 4WD

AASIS MATERIAL # 10123531

VENDOR: BALE CHEVROLET/100095671

MFG & MODEL BID: Chevrolet Silverado Crew (CK10543) with Standard Hitch		$38,028.00

ENGINE & CYLINDERS: 6.0L/V8

PRODUCTION MONTH: January 2009

Approximate Delivery after production date: 8 weeks

Air Bags: Driver & Front Passenger, factory installed

Air Conditioning: factory installed

Alternator: type recommended by manufacturer for vehicle as equipped

Battery: Ni-MH (Nickel-Metal Hybrid)

Battery Voltage: type recommended by manufacturer for vehicle as equipped

Brakes: Each vehicle shall be equipped with the manufacturer's standard power assisted service brakes with a four-wheel, electronic controlled, anti-lock brake system (ABS)

Doors: Two (2) manufacturer's standard type for vehicle

Emissions System: manufacturer's standard type for vehicle

Engine: minimum of 8-cylinder

Floor Mats: front and rear, color to coincide with interior

Glass: manufacturer standard privacy or tinted glass in all windows

GVWR: 7300 lbs

Horsepower, Net: minimum of 295

Inside hood latch control

Keys: 2 sets

License Plate Brackets: front and rear

Operator's Manual

Paint: one (1) exterior color selected from manufacturer's standard list and specified by ordering entity

Payload package for heavy-duty use

Power Steering: factory installed manufacturer's standard power assisted steering

Radio: AM/FM

Seat, Front: 40-20-40 split bench

Seat, Rear Bench: full width, folding, 3-passenger

Suspension: type recommended by manufacturer for vehicle as equipped

Tires and wheels: (four) 4 radial, tubeless tires of the size and load range recommended by vehicle manufacturer for automobile as equipped

Towing Capacity: 5900 lbs

Transmission/Driveline: Each vehicle shall be equipped with the manufacturer's standard automatic-overdrive type transmission and shall include the manufacturer's standard transmission cooler. Vehicles equipped with a continuously variable transmission (CVT) will be acceptable

Upholstery: cloth material and colors to coincide with exterior color chosen

Wheelbase: minimum of 140"

Warranty, Basic: 3 years/36,000 miles

Warranty, Battery: 8 years/100,000 miles

OPTIONAL EQUIPMENT - Purchaser may choose from the following:

HD Trailer Towing Equipment for towing up to 6700 lbs		NA

HD Trailer Towing Equipment for towing up to 7700 lbs		NA

Limited Slip or Locking Differential		STANDARD

Body Side Molding				STANDARD

ITEM 8: TYPE HFU - FIVE (5) PASSENGER 4WD OR ALL WHEEL DRIVE SUV

AASIS MATERIAL #10123533

VENDOR: LONGO TOYOTA/100159321

MFG & MODEL BID: Toyota Highlander					$33,188.00

ENGINE & CYLINDERS: 3.3L/V6

Approximate Delivery after production date: 120 days

Air Bags: Driver & Front Passenger, factory installed

Air Conditioning: factory installed

Alternator: type recommended by manufacturer for vehicle as equipped.

Battery: Ni-MH (Nickel-Metal Hybrid)

Battery Voltage: type recommended by manufacturer for vehicle as equipped

Brakes: Each vehicle shall be equipped with the manufacturer's standard power assisted service brakes with a four-wheel, electronic controlled, anti-lock brake system (ABS).

Doors: Five (5); manufacturer's standard type for vehicle

Emissions System: manufacturer's standard type for vehicle.

Engine: minimum of 4-cylinder

Floor Mats: front and rear, color to coincide with interior.

Glass: manufacturer standard privacy or tinted glass in all windows.

Horsepower, Net: 155 hp

Inside hood latch control

Keys: 2 sets

License plate brackets: front and rear

Operator's Manual

Paint: one (1) exterior color selected from manufacturer's standard list and specified by ordering entity.

Power Outlet

Radio: AM/FM

Seat, Front: bucket

Seat, Second: fold-flat type; manufacturer's standard type for vehicle as equipped.

Power Steering: factory installed manufacturer's standard power assisted steering

Suspension: type recommended by manufacturer for vehicle as equipped.

Tires and wheels: (four) 4 radial, tubeless tires of the size and load range recommended by

vehicle manufacturer for automobile as equipped.

Towing, Class 1: up to 1000 lbs

Transmission/Driveline: Each vehicle shall be equipped with the manufacturer's standard automatic-overdrive type transmission and shall include the manufacturer's standard transmission cooler. Vehicles equipped with a continuously variable transmission (CVT) will be acceptable.

Upholstery: cloth material and colors to coincide with exterior color chosen.

Wheelbase: minimum of 100"

Warranty, Basic: 3 years/36,000 miles

Warranty, Battery: 7 years/100,000 miles

OPTIONAL EQUIPMENT - Purchaser may choose from the following:

Retractable Cargo Area Cover	$85.00

Engine Block Heater 			NA

Daytime Running Lamps		STANDARD

Body Side Molding			NA

ITEM 10: TYPE HSF - SEVEN (7) PASSENGER 4WD OR ALL WHEEL DRIVE SUV

AASIS MATERIAL #10123533

VENDOR: LONGO TOYOTA/100159321

MFG & MODEL BID: Toyota Highlander				$35,488.00

ENGINE & CYLINDERS: 3.3L/V6

Approximate Delivery after production date: 120 days

Air Bags: Driver & Front Passenger, factory installed

Air Conditioning: factory installed

Alternator: type recommended by manufacturer for vehicle as equipped.

Battery: Ni-MH (Nickel-Metal Hybrid)

Battery Voltage: type recommended by manufacturer for vehicle as equipped

Brakes: Each vehicle shall be equipped with the manufacturer's standard power assisted service brakes with a four-wheel, electronic controlled, anti-lock brake system (ABS).

Doors: Five (5) manufacturer's standard type for vehicle

Emissions System: manufacturer's standard type for vehicle.

Engine: minimum of 6-cylinder

Floor Mats: front and rear, color to coincide with interior.

Glass: manufacturer standard privacy or tinted glass in all windows.

Horsepower, Net: 270 hp

Inside hood latch control

Keys: 2 sets

License plate brackets: front and rear

Operator's Manual

Paint: one (1) exterior color selected from manufacturer's standard list and specified by ordering entity.

Power Outlet: 110-volt

Power Steering: factory installed manufacturer's standard power assisted steering

Radio: AM/FM

Seat, Front: bucket

Seat, Second: fold-flat type; manufacturer's standard type for vehicle as equipped.

Seat, 3rd Row: manufacturer's standard type for vehicle as equipped

Suspension: type recommended by manufacturer for vehicle as equipped.

Tires and wheels: (four) 4 radial, tubeless tires of the size and load range recommended by

vehicle manufacturer for automobile as equipped.

Transmission/Driveline: Each vehicle shall be equipped with the manufacturer's standard automatic-overdrive type transmission and shall include the manufacturer's standard transmission cooler. Vehicles equipped with a continuously variable transmission (CVT) will be acceptable.

Upholstery: cloth material and colors to coincide with exterior color chosen.

Wheelbase: minimum of 100"

Warranty, Basic: 3 years/36,000 miles

Warranty, Battery: 7 years/100,000 miles

OPTIONAL EQUIPMENT - Purchaser may choose from the following:

Retractable Cargo Area Cover	$85.00

Engine Block Heater			NA

Daytime Running Lamps		STANDARD

Body Side Molding			NA

1.	STATE AGENCY GUIDELINES FOR ORDERING VEHICLES

All vehicles as defined by Arkansas Code Annotated of 1987 at section §22-8-206, will be ordered by the Department of Finance & Administration, Administrative Services.  Vehicles not covered by Arkansas Code Annotated of 1987 at section §22-8-206, will be ordered by Ordering Agency after notifying the Office of State Procurement. Agencies are strongly advised to place an order as soon as possible due to restrictions on plant capacity and fleet allocations.  Once all orders are filled, you will have to wait for the next opportunity to order.

1.1	ORDERING:  A state agency purchase order(s) and all necessary supporting documents will be sent to:

AR Department of Finance and Administration

Office of Administrative Services

P.O. Box 2485

Little Rock, AR  72203

1.2	OPTIONS:  Purchasers may select preferred options listed and include the information in their procurement request and cannot add options to vehicle purchases.

2.	COOPERATIVE PURCHASING PROGRAM PARTICIPANTS NOTE:

In order to provide the discounted prices offered in this procurement package to both the State and the Cooperative Purchasing Program participants, the vehicle vendors must receive timely payment, payment for partial shipment on multiple vehicle orders, and have all required approvals obtained prior to order placement. All these conditions are being met by state agencies, who are required to have sufficient funds and approvals before orders are placed and to make prompt payment for vehicles as received. It is incumbent upon Cooperative Purchasing participants to have all approvals obtained and funds available to complete the purchasing transaction in a prompt manner. Most of the dealers have fifteen days from the time a vehicle leaves the factory to pay the manufacturers. In order to continue to receive the fleet pricing, you must ensure prompt payment for each vehicle as it is received.  All standard and special terms and conditions listed must be equally applied to such participants.  Agencies are strongly advised to place an order as soon as possible due to restrictions on plant capacity and fleet allocations.  Once all orders are filled, you will have to wait for the next opportunity to order.

2.1	OPTIONS:  Purchasers may select preferred options listed and include the information in their procurement request and cannot add options to vehicle purchases.